SECTION 07430

INSULATED BRICK WALL PANEL SYSTEMS

Display hidden notes to specifier. (Don't know how? Click Here)

Copyright 2018 InsulStone, Inc. - All rights reserved

** NOTE TO SPECIFIER ** CastleRock Building Products, Inc. DBA ICAP-USA and InsulStone insulated panels with porcelain, stone, thin brick, and magnesium oxide fascia.

This section is based on the products of CastleRock Building Products, Inc. manufactured by: ICAP-USA/InsulStone, Inc. which is located at:

300 e. Franklin Rd.

Meridian, ID 83642

Tel: (208) 895-8557

Fax: (208) 639-6422

Email: insulstone@gmail.com, icap.sales@gmail.com

Web: http://www.icap-usa.com , http://www.insulstone.com

ICAP-USA/InsulStone is a pre-engineered, INSULATED CLADDING PANEL (ICP™) system meeting ASTM E84 with zero flame spread and zero smoke generation, NFPA 285, and ASTM E330(2002): “Standard Test Method for Structural Performance for Exterior Windows, Doors, Skylights and Curtain Walls by Static Air Pressure Difference. It has an interlocking tongue and groove connector. It can be installed with screws or staples faster and easier and is much stronger and cost effective than traditional construction methods.

E-84 Series may be installed over OSB or other plywood materials with conventional or liquid applied air/weather resistant barriers. Liquid applied WRB’s are recommended due to the fact they are typically self-sealing around fastener penetrations. NFPA 285 requires approved liquid applied WRB’s.

This cladding installs several times faster than traditional methods, is more cost efficient and can be installed in most any weather conditions. See other specifications for fascia options including Engineered Stone, Porcelain, Thin Brick, Natural Stones, Metal and Magnesium Oxide.

Standard components include flat panels, end/corner panels, window trims, metal starter section and a cap. Accessories may include electrical plates, hose bibs, light bases, and accents.

- GENERAL

SECTION INCLUDES

** NOTE TO SPECIFIER ** Delete items below not required for project.

    - Pre-engineered Insulated Brick cladding panels with continuous insulation tongue and groove interlock and hidden fastener system.

    - Specification includes methods for installation of panels meeting listed fire requirements. following fire requirements:

C.      Insulation Requirements:

R-value: R10

Special R-values _______________

RELATED SECTIONS

** NOTE TO SPECIFIER ** Delete any sections below not relevant to this project; add others as required.

Section 07190 - Water Repellents:  Air/weather Resistive Barriers applied to exterior sheathing surfaces.

Section 07620 - Sheet Metal Flashing and Trim:  Veneer Flashing.

Section 07900 - Joint Sealers:  Perimeter Sealing at Openings.

Brick water proofer and water sealer: Applied over finished brick and mortar.

REFERENCES

** NOTE TO SPECIFIER ** Delete references from the list below that are not actually required by the text of the edited section.

ASTM International (ASTM) & (ULC):

1.ASTM C188-17– Standard Test Method for Thin Veneer Brick made from Clay or 			Shale.

2. ASTM E84 - Standard Test Method for Surface Burning Characteristics of Building 			Materials.

3. ASTM E119 - Standard Test Methods for Fire Tests of Building Construction and 			Materials.

4.ULC S102-07 - Flame Spread and Smoke Generation.

5.ASTM E330 - Standard Test Method for Structural Performance of Exterior Windows, 		Doors, Skylights and Curtain Walls by Uniform Static Air Pressure Difference.

6.NFPA 285 Standard Fire Test Method of Evaluation of Fire Propagation               	Characteristics of Exterior Non-Load-Bearing Wall Assemblies Containing 	Combustible Components, 2012 Edition

IBC - Foam Plastic, Section 2603 IBC, Section R 314 IRC and Sections 3.1, 3.2, 3.6, 3.7, and 4.5.15 of AC12. AC51 Sections 3.6 and 4.2. Freeze/Thaw Resistance

ICC-Evaluation Service (ICC-ES):  ICC-ES AC315 - Criteria for pre-engineered Veneer Systems with Foam Plastic Backing.

ULC S102-07 - Flame Spread and Smoke Generation.

QUALITY ASSURANCE

** NOTE TO SPECIFIER ** Delete if not required.

Pre-Engineered Thin Brick System with Foam Backing. Mfg. by CastleRock Building Products, Inc. (ICAP-USA)

Tested by Intertek Laboratories, W-H Listing Report #20269

Warnock Hersey/ETL third party QA assurance program.

SUBMITTALS

Submit under provisions of Section 01300.

Product Data:  Manufacturer's data sheets on each product to be used, including:

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Installation methods.

Verification Samples:  Submit sample boards of pre-engineered masonry veneer with foam backing.

CLOSEOUT SUBMITTALS

Submit the following in compliance with the requirements of Section 01770.

Maintenance Instructions.

Warranty.

  - QUALITY ASSURANCE

    - Manufacturer Qualifications: Minimum 5-year experience manufacturing similar products.

    - Installer Qualifications:

General Contractor or responsible party is responsible to select an installer meeting the	requirements and certifications required by ICAP-USA CERTIFIED INSTALLER 	PROGRAM and QUALIFIED FOR THE CERTIVICATION LEVEL DESCRIBED 	BELOW:

1.	Level 1Iinstaller: 	Residential projects

Idaho Construction & Handyman LLC.

Richard Rodriguez

Phone:	208-860-8999

Email:	idahoconstruction@gmail.com

Legacy Specialties INC.

Kelly Jensen

Phone: 559-284-4089

Email	kellyj@legacyspc.com

2.	Level 2 Installer:	Light Commercial Projects

a).       Idaho Construction & Handyman LLC.

Richard Rodriguez

Phone:	208-860-8999

Email:	idahoconstruction@gmail.com

b).       Legacy Specialties INC.

Kelly Jensen

Phone: 559-284-4089

Email	kellyj@legacyspc.com

c)

3.	 Level 3 Installer:	NFPA 285 Projects

a).        Idaho Construction & Handyman

Richard Rodriguez

Phone:	208-860-8999

Email:	idahoconstruction@gmail.com

b).	Legacy Specialties INC.

Kelly Jensen

Phone: 559-284-4089

Email	kellyj@legacyspc.com

c).

4.	Level 4 Installer:	Public Works

a).     	Idaho Construction & Handyman LLC.

Public Works # 208.860.8999 (pending)

Richard Rodriguez

Phone:	208-860-8999

Email:	idahoconstruction@gmail.com

b).

c).

Mock-Up: Provide a mock-up for evaluation of surface preparation techniques and application workmanship.

Prepare 4 feet by 4 feet field mock-up at a location on the structure as directed by the Architect or Construction Manager. Use approved materials and colors.

Obtain approval of Architect.

Protect and retain mock-up as a basis for approval of completed work. Approved mock-up may be incorporated into completed work.

** NOTE TO SPECIFIER ** Include a mock-up if the project size and/or quality warrant taking such a precaution. The following is one example of how a mock-up on a large project might be specified. When deciding on the extent of the mock-up, consider all the major different types of work on the project.

PRE-INSTALLATION MEETINGS

Convene minimum two weeks prior to starting work of this section.

DELIVERY, STORAGE, AND HANDLING

Transport, handle, store, and protect products in compliance with the requirements of Section 01600 and manufacturer's recommendations.

Prevent damage or contamination to materials by water, freezing, foreign matter, and other causes.

Handling: Handle materials to avoid damage.

PROJECT CONDITIONS

Keep materials dry prior to installation. Store adhesives at minimum 40 degree F (4.4 degree C) for ease of application.

SEQUENCING

Coordinate lead time for fabrication and delivery with manufacturer.  Order materials to prevent delay of construction progress.  Ensure that products of this section are supplied to affected trades in time to prevent interruption of construction progress.

WARRANTY

Manufacturer’s extended published limited warranty.

EXTRA MATERIALS

Extra Materials:  Furnish extra cladding materials in a variety of shapes and sizes in quantity equal to at least three percent of the installed Cladding.

- PRODUCTS

MANUFACTURERS

Acceptable Manufacturer: ICAP-USA/InsulStone, Inc; 100 S. Adkins Way Suite 104, Meridian, ID 83642.  ASD. Tel: (208) 895-8557.  Fax: (208) 639-6422.  Email: insulstone@gmail.com. Web: http://www.insulstone.com.

** NOTE TO SPECIFIER ** Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

Substitutions: Not permitted.

Requests for substitutions will be considered in accordance with provisions of Section 01600.

BRICK INSULATED PANELS

Pre-Engineered Mortar-Less Brick Panels with Continuous Insulation Tongue and Groove Interlock:  InsulStone by InsulStone.

** NOTE TO SPECIFIER ** Delete if not required.

Brick Panel Description:

Acceptable Thin Brick Manufacturer(s)

** NOTE TO SPECIFIER ** List Acceptable Thin Brick Manufacturer

Brick Size(s):

Size, Flats:  ___ inches x ___ inches (___ mm x ___ mm).

Size, Corners: ___ inches x ___ inches (___ mm x ___ mm).

** NOTE TO SPECIFIER ** List Thin Brick Size(s):

Brick Style(s) or Series:

Style or series:  _________________

Style or series:  _________________

** NOTE TO SPECIFIER ** List Acceptable Styles or Series.

Brick Color(s):

_____________________

_____________________

** NOTE TO SPECIFIER ** List Acceptable Colors or Color #(s).

INSULATED THIN BRICK SIDING PANELS

List Panel Part(s)

Flat Full Panel

Flat ½ Panel

Corner Panel

** NOTE TO SPECIFIER ** Delete panels not required.

Window Trim Top (s):

Full Brick Soldier Course

Narrow Brick

Stone Header

Custom Applications

Window Trim Sides:

Soldier Course

Narrow Soldier Course

Full Soldier Course

Stone Side Trims

Custom Applications

Window Sill:

Soldier Course Brick Window Sill

Stone Window Sill

Custom Applications

Wainscot Cap(s)

Brick

Stone

** NOTE TO SPECIFIER ** Delete if not required.  Delete types and lengths not required.

ACCESSORY MATERIALS

Flashing(s):

Rigid, corrosion-resistant.

Custom Penetration Applications

** NOTE TO SPECIFIER ** Some jurisdictions require weep screeds on wall cladding systems. Delete if not required.

Weep Screed: Corrosion resistant metal a minimum of .019 inches (0.5 mm) or 26 gage in thickness; or plastic weep screed a minimum of 0.050 inch (1.3 mm) with a minimum vertical attachment flange of 3-1/2 inches (89 mm) wide.

- EXECUTION

EXAMINATION

Do not begin installation until substrates have been properly prepared.

If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

Water resistive barrier shall conform to ICC-ES AC38 acceptance criteria.

PREPARATION

Clean surfaces thoroughly prior to installation.

Protection: Prevent work from occurring on the opposite of walls to which s cladding is being applied.

INSTALLATION

Installation as shown on drawings and as specified in accordance with manufacturer’s installation instructions.

Weather-Resistant Barrier:

Installation of weather barrier and wall panels shall comply with local building code requirements or Authority Having Jurisdiction.

Install weather barrier per manufacturer’s installation instructions.

Weather-resistant barrier shall be free of tears or leaks.

Flashing: Install flashing as shown.

Flashing and flashing accessories shall be corrosion resistant materials and integrated with the weather barrier materials. Flashing shall be installed at all through-wall penetrations and at terminations of the panel system, around doors, windows and other protrusions in accordance with local building codes.

Install flashing around penetrations and terminations of the veneer application.

Install flashing to divert water run-off away from the finished surface area.

CLEANING

Cleaning Veneer Units:

Wash with soft bristle brush and water/granulated detergent solution.

Rinse immediately with clean water.

PROTECTION

Protect installed products until completion of project.

Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION