SECTION 07430

INSULATED WALL PANEL SYSTEMS

Display hidden notes to specifier. (Don't know how? Click Here)

Copyright 2015 ARCAT Inc. - All rights reserved

** NOTE TO SPECIFIER **  ICAP-USA/InsulStone, Inc.; cast stone insulated panels, ICAP-USA porcelain clad insulated panels.

This section is based on the products of ICAP-USA/InsulStone, Inc. which is located at:

300 Franklin Rd.

Meridian, ID 83642

Tel: (208) 895-8557

Fax: (208) 639-6422

Email: insulstone@gmail.com, icap.sales@gmail.com

Web: http://www.insulstone.com, http://www.icap-usa.com

{click Here} for additional information.

ICAP-USA/InsulStone is a pre-engineered, insulated panel system with zero flame spread and an interlocking tongue and groove connector. It can be installed with screws or staples faster and easier than traditional lathe and mortar masonry.

ICAP-USA/InsulStone is composed of a high density EPS foam panel with a manufactured or cast stone (or Porcelain) laminated to the energy efficient, flame resistant, interlocking panel and meets the new continuous insulation requirements for siding applications.

This cladding is faster, easier, cost efficient and can be installed in most any weather conditions. Several options include Stone, Porcelain and cementitious fiber boards laminated to the interlocking foam panel. Other applications include manufactured home skirting and exterior wall coverings. Standard insulation values are R-6, R-11, and R-18.

Standard components include flat panels, end/corner panels, metal starter section and a cap. Accessories include electrical plates, hose bibs, light bases, keystones and quoin accents.

- GENERAL

SECTION INCLUDES

** NOTE TO SPECIFIER ** Delete items below not required for project.

Pre-engineered mortar-less cast stone panels with continuous insulation tongue and groove interlock.

Pre-engineered lap siding panels with continuous insulation tongue and groove interlock.

Pre-engineered grouted porcelain panels with continuous insulation tongue and groove interlock.

Pre-engineered non-grouted porcelain panels with continuous insulation tongue and groove interlock.

RELATED SECTIONS

** NOTE TO SPECIFIER ** Delete any sections below not relevant to this project; add others as required.

Section 07190 - Water Repellents:  Optional water repellent coating applied to exterior manufactured stone veneer surfaces.

Section 07620 - Sheet Metal Flashing and Trim:  Veneer Flashing.

Section 07900 - Joint Sealers:  Perimeter Sealing at Openings.

REFERENCES

** NOTE TO SPECIFIER ** Delete references from the list below that are not actually required by the text of the edited section.

ASTM International (ASTM):

ASTM C39 - Standard Test Method for Compressive Strength of Cylindrical Concrete Specimens.

ASTM C192 - Standard Practice for Making and Curing Concrete Test Specimens in the Laboratory.

ASTM C140 - Standard Test Methods for Sampling and Testing Concrete Masonry Units.

ASTM C373 – Standard Test Method for Water Absorption of Porcelain and Ceramic Tiles.

ASTM C648 – Standard Test Method for Breaking Strength of Porcelain and Ceramic Tiles.

ASTM C650 – Standard Test Method for Chemical Resistance of Porcelain and Ceramic Tiles.

ASTM C1027 – Standard Test Method for Abrasion Resistance of Porcelain and Ceramic Tiles.

ASTM E84 - Standard Test Method for Surface Burning Characteristics of Building Materials.

ASTM E119 - Standard Test Methods for Fire Tests of Building Construction and Materials.

ASTM E330 - Standard Test Method for Structural Performance of Exterior Windows, Doors, Skylights and Curtain Walls by Uniform Static Air Pressure Difference.

IBC - Foam Plastic, Section 2603 IBC, Section R 314 IRC and Sections 3.1, 3.2, 3.6, 3.7, and 4.5.15 of AC12. AC51 Sections 3.6 and 4.2. Freeze/Thaw Resistance

ICC-Evaluation Service (ICC-ES):  ICC-ES AC315 - Criteria for pre-engineered Masonry Veneer Systems with Foam Plastic Backing.

ULC S102-07 - Flame Spread and Smoke Generation.

QUALITY ASSURANCE

** NOTE TO SPECIFIER ** Delete if not required.

Pre-Engineered Masonry Veneer System with Foam Backing. W-H Listing 20269 (Intertek) and Intertek third party QA assurance program.

Surface Burning Characteristics (ASTM E-84) (CAN/ULC S102): Flame spread – 0, Smoke developed – 0.

Transverse Load Testing (Wind Load): 126 lbs/psf (6 kPa) per ASTM E330.

SUBMITTALS

Submit under provisions of Section 01300.

Product Data:  Manufacturer's data sheets on each product to be used, including:

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Installation methods.

Verification Samples:  Submit sample boards of pre-engineered masonry veneer with foam backing.

CLOSEOUT SUBMITTALS

Submit the following in compliance with the requirements of Section 01770.

Maintenance Instructions.

Warranty.

QUALITY ASSURANCE

Manufacturer Qualifications: Minimum 5 year experience manufacturing similar products.

Installer Qualifications.

Company with documented experience in installation of continuous insulated wall systems or proof of completion of the factory authorized installer training program.

** NOTE TO SPECIFIER ** Include a mock-up if the project size and/or quality warrant taking such a precaution. The following is one example of how a mock-up on a large project might be specified. When deciding on the extent of the mock-up, consider all the major different types of work on the project.

Mock-Up: Provide a mock-up for evaluation of surface preparation techniques and application workmanship.

Prepare 4 feet by 4 feet field mock-up at a location on the structure as directed by the Architect or Construction Manager. Use approved materials and colors.

Obtain approval of Architect.

Protect and retain mock-up as a basis for approval of completed work. Approved mock-up may be incorporated into completed work.

PRE-INSTALLATION MEETINGS

Convene minimum two weeks prior to starting work of this section.

DELIVERY, STORAGE, AND HANDLING

Transport, handle, store, and protect products in compliance with the requirements of Section 01600 and manufacturer's recommendations.

Prevent damage or contamination to materials by water, freezing, foreign matter, and other causes.

Handling: Handle materials to avoid damage.

PROJECT CONDITIONS

Keep materials dry prior to installation. Store adhesives at minimum 40 degree F (4.4 degree C) for ease of application.

SEQUENCING

Coordinate lead time for fabrication and delivery with manufacturer.  Order materials to prevent delay of construction progress.  Ensure that products of this section are supplied to affected trades in time to prevent interruption of construction progress.

WARRANTY

Manufacturer’s extended published limited warranty.

EXTRA MATERIALS

Extra Materials:  Furnish extra cladding materials in a variety of shapes and sizes in quantity equal to at least three percent of the installed stone.

- PRODUCTS

MANUFACTURERS

Acceptable Manufacturer: ICAP-USA/InsulStone, Inc; 100 S. Adkins Way Suite 104, Meridian, ID 83642.  ASD. Tel: (208) 895-8557.  Fax: (208) 639-6422.  Email: insulstone@gmail.com. Web: http://www.insulstone.com.

** NOTE TO SPECIFIER ** Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

Substitutions: Not permitted.

Requests for substitutions will be considered in accordance with provisions of Section 01600.

CAST-STONE INSULATED PANELS

Pre-Engineered Mortar-Less Cast Stone Panels with Continuous Insulation Tongue and Groove Interlock:  InsulStone by InsulStone.

** NOTE TO SPECIFIER ** Delete if not required.

Stacked Stone Flats:

Size:  5.75 inches x 22 inches (146 mm x 559 mm).

** NOTE TO SPECIFIER ** Delete pattern not required.

Pattern: Sand.

Pattern: Autumn.

Pattern: Canyon.

Pattern: Mountain.

Pattern: Rundle.

Pattern: Canadian Rundle.

** NOTE TO SPECIFIER ** Delete if not required.

Limestone:

Size, Flats:  5.75 inches x 22 inches (146 mm x 559 mm).

Size, Double Panel:  11.5 inches x 22 inches (292 mm x 559 mm).

** NOTE TO SPECIFIER ** Delete pattern not required.

Pattern: Ivory/Rose.

Pattern: Autumn.

Pattern: Canyon.

Pattern: Mountain.

Pattern: Rundle.

** NOTE TO SPECIFIER ** Delete if not required.

Ledge Stone Series:

Size:  5.75 inches x 22 inches (146 mm x 559 mm).

** NOTE TO SPECIFIER ** Delete pattern not required.

Pattern: Cold Springs.

Pattern: Warm Springs.

Pattern: Hot Springs.

Pattern: Mountain Springs.

Pattern: Black Springs.

** NOTE TO SPECIFIER ** Delete if not required.

Ledge stone/Field stone blend.

** NOTE TO SPECIFIER ** Delete if not required.

INSULATED LAP SIDING PANELS

Pre-Engineered Lap Siding Porcelain Panels with Continuous Insulation Tongue and Groove Interlock:  ICap by InsulStone.

Pre-engineered lap siding panels with continuous insulation tongue and groove interlock.

Width: 8 inches (203 mm).

Length: 36 inches (914 mm).

Length: 47-3/4 inches (1213 mm).

Length: 71 inches (1803 mm).

Length: 96 inches (______mm).

** NOTE TO SPECIFIER ** Delete thickness not required.

Thickness R-10: 2.625 inches (66 mm).

Thickness R-17: 4.00 inches (101 mm).

** NOTE TO SPECIFIER ** Delete sizes not required.  Special sizes are available up to 24 by 96 inches.

Size:  12 inches x 24 inches (305 mm x 610 mm).

Size:  17 inches x 35 inches (432 mm x 889 mm).

Size:  19 inches x 39 inches (482 mm x 990 mm).

Size:  24 inches x 48 inches (610 mm x 1219 mm).

Size:  24 inches x 72 inches (610 mm x 1829 mm).

Size:  24 inches x 96 inches (610 mm x 2438 mm).

Size, Custom:  ______.

** NOTE TO SPECIFIER ** Delete if not required.

Window Trim Size:  3-3/4 inches x 48 inches (95 mm x 1219 mm).

Window Trims Size:  3-3/4 inches x 72 inches (95 mm x 1819 mm).

Window Trims Size:  3-3/4 inches x 96 inches (95 mm x 2438 mm).

** NOTE TO SPECIFIER ** Delete if not required.  Delete types and lengths not required.

3-D Pop-Outs:  8 inches (203 mm) wide.

Length:  36 inches (914 mm).

Length:  48 inches (1219 mm).

Length:  60 inches (1524 mm).

Length:  72 inches (1829 mm).

Length:  96 inches (2438 mm).

3-D Pop-Outs:  12 inches (305 mm) wide.

Length:  36 inches (914 mm).

Length:  48 inches (1219 mm).

Length:  60 inches (1524 mm).

Length:  72 inches (1829 mm).

Length:  96 inches (2438 mm).

3-D Pop-Outs:  24 inches (610 mm) wide.

Length:  36 inches (914 mm).

Length:  48 inches (1219 mm).

Length:  60 inches (1524 mm).

Length:  72 inches (1829 mm).

Length:  96 inches (2438 mm).

** NOTE TO SPECIFIER ** Delete if not required.

Wood Grain Series:

** NOTE TO SPECIFIER ** Delete pattern not required.

Pattern: Sandlewood.

Pattern: Alder.

Pattern: Hickory.

Pattern: Spruce.

Pattern: Weathered Cedar.

Pattern: Weathered Barnwood.

Pattern: Mahogany.

Pattern: Teak.

Pattern: Theory 1.

Pattern: Theory 2.

Pattern: Theory 3.

** NOTE TO SPECIFIER ** Delete if not required.

Marble Series:

** NOTE TO SPECIFIER ** Delete pattern not required.

Pattern: Spa.

Pattern: Paonazzetto.

Pattern: Himachal White.

Pattern: Imperial.

Pattern: Antique.

Pattern: Travertino.

** NOTE TO SPECIFIER ** Delete if not required.

Granite Series:

** NOTE TO SPECIFIER ** Delete pattern not required.

Pattern: Linen.

Pattern: Café.

Pattern: Auburn.

Pattern: Noce.

Pattern: Grigio.

Pattern: Alchemy Silver.

Pattern: Bianco.

Pattern: Chiara.

Pattern: Nico.

Pattern: Advance.

Pattern: Cue.

Pattern: Drift.

Pattern: Gesture.

Pattern: Signal.

** NOTE TO SPECIFIER ** Delete if not required.

Solid Series:

** NOTE TO SPECIFIER ** Delete pattern not required.

Pattern: True White

Pattern: Arctic.

Pattern: Sequoia

Pattern: Redwood.

Pattern: Arcadia.

Pattern: True Black.

Pattern: Modena.

INSULATED GROUTED PORCELAIN PANELS

Pre-Engineered Grouted Porcelain Panels with Continuous Insulation Tongue and Groove Interlock:  ICap by InsulStone.

Width: 8 inches (203 mm).

** NOTE TO SPECIFIER ** Special order: Up to 24 x 144 inches Special order.  Delete lengths not required.

Length: 36 inches (914 mm).

Length: 47-3/4 inches (1213 mm).

Length: 71 inches (1803 mm).

** NOTE TO SPECIFIER ** Delete thickness not required.

Thickness R-10: 2.625 inches (66 mm).

Thickness R-17: 4.00 inches (101 mm).

** NOTE TO SPECIFIER ** Delete sizes not required.  Special sizes are available up to 24 by 96 inches.

Size:  12 inches x 24 inches (305 mm x 610 mm).

Size:  17 inches x 35 inches (432 mm x 889 mm).

Size:  24 inches x 48 inches (610 mm x 1219 mm).

Size:  24 inches x 60 inches (610 mm x 1524 mm).

Size:  24 inches x 72 inches (610 mm x 1829 mm).

Size:  24 inches x 96 inches (610 mm x 2438 mm).

Size, Custom:  ______.

** NOTE TO SPECIFIER ** Delete if not required.

Window Trim Size:  3-3/4 inches x 48 inches (95 mm x 1219 mm).

Window Trims Size:  3-3/4 inches x 72 inches (95 mm x 1819 mm).

Window Trims Size:  3-3/4 inches x 96 inches (95 mm x 2438 mm).

** NOTE TO SPECIFIER ** Delete if not required.  Delete types and lengths not required.

3-D Pop-Outs:  8 inches (203 mm) wide.

Length:  36 inches (914 mm).

Length:  48 inches (1219 mm).

Length:  60 inches (1524 mm).

Length:  72 inches (1829 mm).

Length:  96 inches (2438 mm).

3-D Pop-Outs:  12 inches (305 mm) wide.

Length:  36 inches (914 mm).

Length:  48 inches (1219 mm).

Length:  60 inches (1524 mm).

Length:  72 inches (1829 mm).

Length:  96 inches (2438 mm).

3-D Pop-Outs:  24 inches (610 mm) wide.

Length:  36 inches (914 mm).

Length:  48 inches (1219 mm).

Length:  60 inches (1524 mm).

Length:  72 inches (1829 mm).

Length:  96 inches (2438 mm).

** NOTE TO SPECIFIER ** Delete if not required.

Wood Grain Series:

** NOTE TO SPECIFIER ** Delete pattern not required.

Pattern: Sandlewood.

Pattern: Alder.

Pattern: Hickory.

Pattern: Spruce.

Pattern: Weathered Cedar.

Pattern: Weathered Barnwood.

Pattern: Mahogany.

** NOTE TO SPECIFIER ** Delete if not required.

Marble Series:

** NOTE TO SPECIFIER ** Delete pattern not required.

Pattern: Spa.

Pattern: Paonazzetto.

Pattern: Himachal White.

Pattern: Imperial.

Pattern: Antique.

Pattern: Travertino.

** NOTE TO SPECIFIER ** Delete if not required.

Granite Series:

** NOTE TO SPECIFIER ** Delete pattern not required.

Pattern: Linen.

Pattern: Café.

Pattern: Auburn.

Pattern: Noce.

Pattern: Grigio.

Pattern: Alchemy Silver.

Pattern: Bianco.

Pattern: Chiara.

Pattern: Nico.

Pattern: Advance.

Pattern: Cue.

Pattern: Drift.

Pattern: Gesture.

Pattern: Signal.

** NOTE TO SPECIFIER ** Delete if not required.

Solid Series:

** NOTE TO SPECIFIER ** Delete pattern not required.

Pattern: True White.

Pattern: Arctic.

Pattern: Sequoia

Pattern: Redwood.

Pattern: Arcadia.

Pattern: True Black.

Pattern: Modena.

** NOTE TO SPECIFIER ** Delete if not required.

INSULATED UN-GROUTED PORCELAIN PANELS

Pre-Engineered Grouted Porcelain Panels with Continuous Insulation Tongue and Groove Interlock:  ICap by InsulStone.

Width: 8 inches (203 mm).

** NOTE TO SPECIFIER ** Special order: Up to 24 x 144 inches Special order.  Delete lengths not required.

Length: 36 inches (914 mm).

Length: 47-3/4 inches (1213 mm).

Length: 71 inches (1803 mm).

** NOTE TO SPECIFIER ** Delete thickness not required.

Thickness R-10: 2.625 inches (66 mm).

Thickness R-17: 4.00 inches (101 mm).

** NOTE TO SPECIFIER ** Delete sizes not required.  Special sizes are available up to 24 by 96 inches.

Size:  12 inches x 24 inches (305 mm x 610 mm).

Size:  17 inches x 35 inches (432 mm x 889 mm).

Size:  19 inches x 39 inches (482 mm x 990 mm).

Size:  24 inches x 48 inches (610 mm x 1219 mm).

Size:  24 inches x 72 inches (610 mm x 1829 mm).

Size:  24 inches x 96 inches (610 mm x 2438 mm).

Size, Custom:  ______.

** NOTE TO SPECIFIER ** Delete if not required.

Window Trim Size:  3-3/4 inches x 48 inches (95 mm x 1219 mm).

Window Trims Size:  3-3/4 inches x 72 inches (95 mm x 1819 mm).

Window Trims Size:  3-3/4 inches x 96 inches (95 mm x 2438 mm).

** NOTE TO SPECIFIER ** Delete if not required.  Delete types and lengths not required.

3-D Pop-Outs:  8 inches (203 mm) wide.

Length:  36 inches (914 mm).

Length:  48 inches (1219 mm).

Length:  60 inches (1524 mm).

Length:  72 inches (1829 mm).

Length:  96 inches (2438 mm).

3-D Pop-Outs:  12 inches (305 mm) wide.

Length:  36 inches (914 mm).

Length:  48 inches (1219 mm).

Length:  60 inches (1524 mm).

Length:  72 inches (1829 mm).

Length:  96 inches (2438 mm).

3-D Pop-Outs:  24 inches (610 mm) wide.

Length:  36 inches (914 mm).

Length:  48 inches (1219 mm).

Length:  60 inches (1524 mm).

Length:  72 inches (1829 mm).

Length:  96 inches (2438 mm).

** NOTE TO SPECIFIER ** Delete if not required.

Wood Grain Series:

** NOTE TO SPECIFIER ** Delete pattern not required.

Pattern: Sandlewood.

Pattern: Alder.

Pattern: Hickory.

Pattern: Spruce.

Pattern: Weathered Cedar.

Pattern: Weathered Barnwood.

Pattern: Mahogany.

Pattern: Teak.

Pattern: Theory 1.

Pattern: Theory 2.

Pattern: Theory 3.

** NOTE TO SPECIFIER ** Delete if not required.

Marble Series:

** NOTE TO SPECIFIER ** Delete pattern not required.

Pattern: Spa.

Pattern: Paonazzetto.

Pattern: Himachal White.

Pattern: Imperial.

Pattern: Antique.

Pattern: Travertino.

** NOTE TO SPECIFIER ** Delete if not required.

Granite Series:

** NOTE TO SPECIFIER ** Delete pattern not required.

Pattern: Linen.

Pattern: Café.

Pattern: Auburn.

Pattern: Noce.

Pattern: Grigio.

Pattern: Alchemy Silver.

Pattern: Bianco.

Pattern: Chiara.

Pattern: Nico.

Pattern: Advance.

Pattern: Cue.

Pattern: Drift.

Pattern: Gesture.

Pattern: Signal.

** NOTE TO SPECIFIER ** Delete if not required.

Solid Series:

** NOTE TO SPECIFIER ** Delete pattern not required.

Pattern: True White

Pattern: Arctic.

Pattern: Sequoia

Pattern: Redwood.

Pattern: Arcadia.

Pattern: True Black.

Pattern: Modena.

ACCESSORY MATERIALS

Flashing:  Rigid, corrosion-resistant.

** NOTE TO SPECIFIER ** Some jurisdictions require weep screeds on wall cladding systems. Delete if not required.

Weep Screed: Corrosion resistant metal a minimum of .019 inches (0.5 mm) or 26 gage in thickness; or plastic weep screed a minimum of 0.050 inch (1.3 mm) with a minimum vertical attachment flange of 3-1/2 inches (89 mm) wide.

Fasteners:

** NOTE TO SPECIFIER ** Delete fastener not required.

Over 7/16 inch OSB plywood or similar sheathing:

Staples: Corrosions resistant, galvanized or stainless 15/16 minimum (23.8 mm) crown by 2 inches (51 mm) leg to penetrate a minimum of 1/2 inch (13 mm) into the sheathing, installed per the manufacturer’s instructions.

Over Metal Studs on 16 inches (406 mm) centers:

# 8 diameter Corrosion-resistant, self-drilling, self-tapping screw with minimum washer or washer head diameter of 3/4 inch (19 mm) diameter and a screw of a suitable length to penetrate the through the foam panel and to obtain 3/8 inch (9.5 mm) penetration beyond inside surface of metal, or 1 inch penetration into wood studs installed per the manufacturer’s instructions.

Over Gypsum Board, Sheetrock Type X or similar on 16 inches (406 mm) centers:

# 8 diameter corrosion resistant screw with a washer or washer head with diameter of 3/4 inch (19 mm) and of a suitable length to penetrate through the foam panel and Gypsum board or similar sheathing into the wood stud a minimum of 1.0 inch (25 mm), or to penetrate the through the foam panel and to obtain 3/8 inch (9.5 mm) penetration beyond inside surface of metal, installed per the manufacturer’s instructions.

- EXECUTION

EXAMINATION

Do not begin installation until substrates have been properly prepared.

If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

Water resistive barrier shall conform to ICC-ES AC38 acceptance criteria.

PREPARATION

Clean surfaces thoroughly prior to installation.

Protection: Prevent work from occurring on the opposite of walls to which s cladding is being applied.

INSTALLATION

Installation as shown on drawings and as specified in accordance with manufacturer’s installation instructions.

Weather-Resistant Barrier:

Installation of weather barrier and wall panels shall comply with local building code requirements or Authority Having Jurisdiction.

Install weather barrier per manufacturer’s installation instructions.

Weather-resistant barrier shall be free of tears or leaks.

Flashing: Install flashing as shown.

Flashing and flashing accessories shall be corrosion resistant materials and integrated with the weather barrier materials. Flashing shall be installed at all through-wall penetrations and at terminations of the panel system, around doors, windows and other protrusions in accordance with local building codes.

Install flashing around penetrations and terminations of the veneer application.

Install flashing to divert water run-off away from the finished surface area.

CLEANING

Cleaning Veneer Units:

Wash with soft bristle brush and water/granulated detergent solution.

Rinse immediately with clean water.

PROTECTION

Protect installed products until completion of project.

Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION